## Slide 1: XR Industrial Project 2 SIF400 AR system 13.01.2026
Hamza Sallam
Eric Márquez
Leon Saidavi
Jorge Luis Botero

## Slide 2: The concept
Enhancing the SIF 400 Line user experience by providing:
Live operational data
AI-driven image recognition.
Key technologies: Hololens2, Unity, APIs, image recognition.

## Slide 3: Project Overview What We Built:
An end-to-end smart manufacturing monitoring system combining:
Industrial automation (SMC SIF-402/405 stations)
Real-time data middleware (Node-RED)
Augmented Reality visualization (HoloLens 2)
AI image recognition system
Key Innovation: Hands-free, real-time monitoring of industrial processes through AR glasses with AI-assisted quality control

## Slide 4: Development Process Phase 1 Phase 3 Phase 2 Phase 4
Planning & Architecture
Integration & Testing
Parallel Development
Production Deployment

## Slide 5: OPC UA Technologies Used: Node-RED AI Vision Unity SMC SIF-402/405 HoloLens 2
Siemens PLCs
Unity 2022.3 + MRTK 2.8.3
Production Machines
Container classification model

## Slide 6: System Architecture
VISUALIZATION
Layer 4
HoloLens 2
MIDDLEWARE
Layer 2: Node-RED
(Running on a Server)
AI Vision
Layer 3
Unity + MRTK + C#
Industrial
Layer 1
SMC Machines SIF-402 and SIF-405
APPLICATION
Notes: Layer 1
Binary object-oriented format
Layer 2
In node-red three flows were implemented, each one:
Collecting data via OPC-UA from the respective station PLC
transform and group data into JSON format to standardize messaging to upper layers
define API endpoint within node-red, through which the data is accesible by Unity scripts
Layer 3: Unity Application (570+ lines C#)
ApiDataManager: Contioue-based polling every 3 seconds
Modular Design: Swappable mock/live data providers
Layer 4:
Frontend of our application
HoloLens 2 Visualization

## Slide 7: Key Features & Capabilities
Developer-Friendly
Intelligent Features
Industrial Integration
Augmented Reality
Monitoring
Notes: 1
Live hopper level and caps counts
Instant alarm notifications
2
Natural hand gestures for interaction
Spatial UI positioned in 3D space
Color-coded status indicators
3
OPC UA protocol support that is Compatible with Siemens PLCs
Zero production interruption
Scalable to multiple machines
4
AI-powered quality control
Automated defect detection
5
Modular architecture
Mock data for offline development
Comprehensive error handling

## Slide 8: Performance & Results
Code Metrics:
Unity: 570+ lines of C# across 7 modular scripts
Key Achievements
✓ Production-ready deployment on HoloLens 2
✓ Real-time visualization of industrial equipment data
✓ Hands-free operation for factory floor
✓ Scalable architecture for additional machines
System performance
API latency <100ms
Data refresh 3 seconds
Hand Tracking <20ms latency

## Slide 9: Technical Challenges Multilayer network MRTK INTERACTION Build configuration 01 03 02
Build Type set to "XAML" instead of "D3D Project"
Missing network capabilities across 4 layers.
Missing MRTK-specific components
Notes: 1.
Solution:
Unity: Allow HTTP downloads and Enable PrivateNetworkClientServer
Node-red, windows firewall: Allow port 1880
2.
Solution: Implemented 4-component stack per button:
Interactable (state management)
PressableButton (press detection)
NearInteractionTouchable (hand proximity)
Box Collider (physics boundary)
Impact: Natural hand-based interaction
3.
Changed Unity build settings, complete rebuild
Impact: Enabled full spatial computing model
Others: Versioning control: Github features novelty for the team.

## Slide 10: Video overview!

## Slide 11: Computer Vision
Adding the final phase, about what the machine does not know

## Slide 12: Why We Build AI Machine data only shows internal states Missing critical setup information: These conditions directly affect safety & correctness
Is there a cup?
What type of cup?
Is the machine physically on or off?
→ We add AI-based visual understanding

## Slide 13: Data & Labeling Collected images of real working scenarios
Labeled all data using Roboflow
Trained costum model
1
2
3

## Slide 14: Training the AI Model Metrics
[{'predictions': {'image': {'width': 1920, 'height': 1088}, 'predictions': [{'width': 30.0, 'height': 44.0, 'x': 1088.0, 'y': 751.0, 'confidence': 0.7976822853088379, 'class_id': 2, 'class': 'round_cup', 'detection_id': '05b8aa1a-b6d0-4701-83de-19d797fc06fd', 'parent_id': 'image'}]}}]
MAP@50 -> 98.1%
Precision -> 96.8%
Recall -> 92.3%
385 Images, Split 90/5/5

## Slide 15: System Integration
AI runs on one computer
Detection results sent to another computer
XR system uses this information to validate setup
Adds environmental awareness to the digital twin

## Slide 16: System Requirements Stable Internet Connection Camera System XR Hardware Computing Infrastructure
Required for AI model inference and communication between components
For capturing the physical environment and providing input to the AI model
XR headset or compatible device for visualization and interaction
Server or workstation to run Node-RED, AI model, and Docker containers

## Slide 17: Operational Impact in the Industry
Operational Uptime
AI-driven diagnostics and troubleshooting
Contextual preemptive guidance
Enhanced Workforce
Scalable JIT training
Streamlined operation: crucial data available, no retrieval efforts.
Quality assurance
Training's performance can be messured.
Updates In the training can be deployed instantly.

## Slide 18: Potential ROI improvements 20-30% 40-60% 30-50%
Aug. Reality training faster to deploy and perform.
Faster training
Error avoidance, higher mean-time to repair
Less downtime
Decreased error rates.
Training effectiveness
https://www.ptc.com/en/resources/augmented-reality/infographic/industrial-ar-high-tech-manufacturing
https://www.microsoft.com/en-us/dynamics-365/blog/business-leader/2022/03/24/manufacturers-are-mitigating-disruptions-with-hololens-2-and-dynamics-365-mixed-reality-solutions/
https://www.automation.com/article/real-roi-ar-manufacturing-beyond-hype

## Slide 19: Ethical Challenges Privacy Health Exploitation 01 03 02
Companies could push efficiency to limits that are unsustainable for workers, and make layoff decisions based on these metrics.
Users could be tracked in every movement, action and comment they make.
Extended use of xR devices have negative and still not fully understood health consequences.

## Slide 20: Trends 02
You can enter a subtitle here if you need it

## Slide 21: Elevated investments Custom infrastructure Lacking connectivity Fragmented tech frameworks Ethical concerns Regulation gray-zone
Critical Challenges for massive adoption

## Slide 22: Our project's limitations
Aging technology (HoloLens2 Discontinued)
Interfacing: 100% custom made.
Abandoned or deprecated repositories.
Lacking documentation.
SIF 400's rudimentary external communication
Image recognition requires vast computing power and/or cloud services.
APIs creation and maintenance is resource intensive.
Extended use poses adoption challenges.
Commercially available gear has low energy autonomy and processing power.

## Slide 23: What we learned as a Team
System integration is significantly more challenging than building individual components
Agile development principles (Scrum) helped keep the team aligned and aware of progress
Clear task distribution increased development efficiency
Continuous testing was essential when combining XR, AI, and machine data
Communication across technical domains (AI, XR, IoT) was critical for success
Early prototyping helped identify system limitations and risks

## Slide 24: Thank you for listening!